## Slide 1: React on a Micro Controller
Mair Swartz

## Slide 2: About me Mair Swartz
Full stack developer
Embedded developer
Tech Lead at HackHunter

## Slide 3: React’s typical address
Where does a deployed React usually live?

## Slide 4: The new address! Why?
Cool factor 😎
Direct control over microprocessor. Which gives us a …
Gateway for React developers to interact with the physical universe

## Slide 5: How
Save React application to chip
Create a web server to expose routes
Create an API layer to work with peripherals

## Slide 6: ESP32 Quick Intro
Dual core
Wi-Fi “Built in”
320 KiB Ram
4 Mb Flash
Lots of peripherals
Low power
ESP32
Flash

## Slide 7: Use cases for React with the ESP32
Direct Interaction
  Remote control
Active monitoring
  Dashboards
Configuration
  Capturing and adjusting information

## Slide 8: Demo

## Slide 9: Learn ESP32.COM
Full course on learning the ESP32

## Slide 10: Recipe
Here are the steps to create a prototype:

## Slide 11: Create a prototype
Plan
1
Plan your design
Research hardware
Prototype
2
Get some hardware
Wire up a breadboard
Configure the chip
3
Allocate space for code and the React app
Program the chip
4
Connect to Wi-Fi
Create server endpoints for your API
Create a React application
5
Create pages
Proxy requests to the chip
Build the app
Flash the app onto the chip
6
Create wild card endpoints to serve React

## Slide 12: Plan
Plan in accordance with the use cases

## Slide 13: Prototype
Wire up a basic circuit

## Slide 14: Configure the chip
C code for web server
React web site
…

## Slide 15: Code your chip
Connect to Wi-Fi
Create server endpoints for your API
Create wild card endpoints to serve react

## Slide 16: Basic server endpoint
void init_server()
{
httpd_config_t config = HTTPD_DEFAULT_CONFIG();
httpd_handle_t server
httpd_start(&server, &config);
httpd_uri_t get_hello_world = {
.uri = "/api/hello-world",
.method = HTTP_GET,
.handler = on_hello_world};
httpd_register_uri_handler(server, &get_hello_world);
}
esp_err_t on_hello_world(httpd_req_t *req)
{
httpd_resp_sendstr(req, "hello world 👋👋👋 😁");
return ESP_OK;
}

## Slide 17: Server endpoints also support Web Sockets
httpd_uri_t btn_push_url = {
.uri = "/ws-api/btn-push",
.method = HTTP_GET,
.handler = on_web_socket_btn_push_url,
.is_websocket = true};
httpd_register_uri_handler(server, &btn_push_url);

## Slide 18: Create the React application
Use proxy for quick development
Add your favorite style library
Add your dependencies.
Keep an eye on your build size

## Slide 19: Size matters
Examining different React templates
Package | Build size
Gatsby | 1.01 Mb
Next .js | 6.34 Mb
Create React APP | 504 KiB
Vite - React | 136 Kib
Vite - Preact | 17.5 Kib

## Slide 20: React Client walkthrough
Basic component using HTTP
Basic component using web sockets
Use proxy for quick development
Add your favorite style library
Add your dependencies.
Keep an eye on your build size

## Slide 21: Demo
Using Chip endpoints
Using a dev server
Using a proxy

## Slide 22: Potential project?
Modular hardware with API’s
Package manager
Common API format
Documentation
Market place

## Slide 23: Thank You
Mair Swartz
Info@learnesp32.com
https://learnesp32.com